## Slide 1: Embedded Programming and Robotics
Lesson 11
Arduino Interrupts

## Slide 2: Interrupts Overview
An interrupt is a hardware event
The processor stops what it was doing and calls the code at a specific location, determined by the type of interrupt
Further interrupts are disabled
The Interrupt Service Routine (ISR) must save state, then restore it upon return (Arduino does this for you)
Timing is critical; ISRs must execute very quickly

## Slide 3: Interrupts Overview
Most Arduino programs poll various sensors, and the Arduino can do this quickly
This is costly because the program must read the device whether data is present or not
Interrupts can make your program far more responsive

## Slide 4: Available Interrupts
On the Arduino Uno we’re using, only pins 2 and 3 can cause interrupts
Thus you can have two different service routines for two different sensors
The Mega has six available interrupts

## Slide 5: Interrupt Service Routines
Use the following function to link a service routine to an interrupt:
attachInterrupt(interrupt, ISR, mode)
Interrupt is either 0 or 1, which is pin 2 or 3 on the Uno
ISR is the name of the interrupt service routine
Mode is one of the following:
  LOW to trigger the interrupt whenever the pin is low,
  CHANGE to trigger the interrupt whenever the pin changes value
  RISING to trigger when the pin goes from low to high,
  FALLING for when the pin goes from high to low.

## Slide 6: Interrupt Service Routines
ISRs take no parameters and return no values
Variables modified by ISRs should be declared as volatile
volatile int mscount;
attachInterrupt(0, increment, RISING);

## Slide 7: Interrupt Service Routines
void increment()
{
mscount++;
}

## Slide 8: Sample Program
People can perceive events that take longer than a specific duration
Write a program that turns on an LED for a variable number of milliseconds, then off for 2 seconds. Start at 1 millisecond
Write an interrupt service routine that, when a switch is pressed, increments the number of milliseconds by 1
Press the switch until you notice that the LED blinks
If you have time, connect the LCD panel to show the “on” time so you don’t have to count button presses